## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID – SIH26170
Problem Statement Title- AI-Driven Anomaly Detection in Component Burn-In & Screening
Theme- Smart Automation
PS Category- Software
Team ID- (enter SIH portal Team ID)
Team Name – Pioneers

## Slide 2: AETHER
Proposed Solution (Describe your Idea/Solution/Prototype)
AETHER: lot-aware PAT outlier screen + 24 h → 168 h drift predictor. After 24 h of 125°C burn-in it returns PASS / HOLD / REJECT plus an inspector brief in engineering English.
Working prototype: Streamlit QA workstation with Lot board, QA inspector, Screen-my-data, judging rubric. Public demo on Render / Streamlit Cloud.
Detailed explanation of the proposed solution
Module A — dynamic outliers: robust PAT (median + 6 × 1.4826 × MAD, AEC-Q001), Isolation Forest, robust Mahalanobis. Scores are lot-normalised so a fast process corner is not scrapped.
Module B — drift: Ridge (inspectable) + optional HGB blend forecasts 168 h from 0 h and 24 h only. Flags if predicted slope > healthy 95th percentile or forecast crosses 90% of the datasheet cap.
How it addresses the problem
Static 50 µA datasheet PASS on a 45 µA part in a 10 µA lot (SIH example LOTSIH-0045). Dynamic PAT REJECTS it. Latent drift is pulled at 24 h instead of escaping into a payload.
Innovation and uniqueness of the solution
Two-signal REJECT (PAT or unsafe drift) — a lone Isolation Forest twitch cannot kill a flight part. HOLD band (not scrap/release). FN cost 1000 vs FP 12. Ridge waterfalls a QA inspector can argue with.
Held-out lots (24 lots, 4,945 parts, split by lot): 100% recall (0 miss / 102 latent defects), 24 h REJECT precision 98.7%, IDDQ 168 h MAE 0.51 µA vs 1.26 µA linear extrapolation.
Pioneers

## Slide 3: TECHNICAL APPROACH
Technologies to be used (programming languages, frameworks, hardware)
Python 3.12 · scikit-learn (IsolationForest, MinCovDet, RidgeCV, HistGradientBoosting) · pandas / NumPy · joblib frozen bundle
Streamlit + Plotly QA workstation · pytest · GitHub Actions-ready scripts (train.py, evaluate.py, predict_realtime_iddq.py)
No extra hardware: laptop / 512 MB web instance. Optional ATE CSV ingest. Deploy: Render Blueprint + Streamlit Community Cloud
Methodology and process for implementation (flow / working prototype)
1. Physics-informed lots (0 / 24 / 96 / 168 h IDDQ, leakage, tpd) — ISRO flight data is not public
2. Split by LOT (not by part) → train Module A + Module B on train lots, freeze on val, score unseen test lots
3. Inference uses only 0 h and 24 h. 96 h / 168 h stay hidden at the early gate
4. Fusion: outlier_score = 0.40 PAT + 0.35 Isolation Forest + 0.25 Mahalanobis → PASS | HOLD | REJECT
Flow: Lot CSV → PAT / IF / Mahalanobis + 168 h forecast → decision + traveller brief → QA override
Prototype live: Screen-my-data tab (upload lot or one part vs a reference lot). Pinned example LOTSIH-0045.
Pioneers

## Slide 4: FEASIBILITY AND VIABILITY
Analysis of the feasibility of the idea
Software-only. Models already trained; artifacts in data/ and models/. Dashboard opens without a GPU.
Fits SIH 36-hour finale: train.py / evaluate.py / Streamlit. Tests encode the official 10 µA / 45 µA / 50 µA example.
No ITAR data needed. Production path: ATE CSV / STDF → freeze PAT k and safety slope on a qualification lot.
Potential challenges and risks
False REJECT if the “lot” mixes process corners (fast + slow wafers labelled as one lot).
Isolation Forest contamination and PAT k = 6 are policy knobs — a cleaner line may want them tighter or looser.
Unit mix-up (nA vs µA) or swapped 0 h / 24 h columns looks like a lot excursion.
Strategies for overcoming these challenges
Lot identity must be real. Two-signal REJECT. QA lead can force HOLD — software is not the last word on a Class-1 part.
Unit / serial checks before scoring. Retrain on a known-good historical set when labels are absent.
HOLD at 96 h instead of scrap/release so expensive space-grade silicon is not thrown away on a borderline score.
Pioneers

## Slide 5: IMPACT AND BENEFITS
Potential impact on the target audience
ISRO / Department of Space screening houses, ATE operators, and QA inspectors who today apply static datasheet limits.
Catches latent escapes a 50 µA cap misses (textbook: 45 µA in a 10 µA lot → static PASS, dynamic REJECT).
Held-out: 0 false negatives / 102 latent defects; 1,172 PASS · 202 HOLD · 75 REJECT; 10,800 chamber-hours recovered from early REJECT.
Benefits of the solution (social, economic, environmental)
Mission / social: fewer infant-mortality failures in flight payloads — the FN the problem statement penalises.
Economic: 144 h of 125°C soak freed per early REJECT; HOLD protects costly space-grade parts from a two-class scrap policy.
Environmental: less wasted high-temperature chamber energy on parts that will fail by 168 h anyway.
Explainability (SIH rubric): robust z vs lot, PAT hits, predicted slope vs healthy 95th percentile, Ridge feature waterfalls.
Pioneers

## Slide 6: RESEARCH AND REFERENCES
Details / Links of the reference and research work
[1] SIH26170 — AI-Driven Anomaly Detection in Component Burn-In & Screening, ISRO / DoS. https://sih2026.vuce.in/ps/SIH26170
[2] AEC-Q001 Rev-D, Guidelines for Part Average Testing (robust mean ± 6 robust sigma / DPAT).
[3] MIL-STD-883 Test Method 1015, Burn-in Test · [4] MIL-PRF-38535 Class Q / V screening (160–240 h at 125°C).
[5][6] Hawkins, Soden et al. — IDDQ testing of CMOS defects (IEEE Trans. Ind. Electron. 1989; IDDQ Testing of VLSI Circuits, 1992).
[7] Nigh et al., Failure analysis of timing and IDDq-only failures, SEMATECH, ITC 1998 (12 confirmed-defect ICs used as a real check).
[8] Liu, Ting, Zhou — Isolation Forest, IEEE ICDM 2008. [9] Rousseeuw & van Driessen — MinCovDet, Technometrics 1999.
[12] Hoerl & Kennard — Ridge Regression, Technometrics 1970. [13] Friedman — Gradient boosting, Ann. Statist. 2001.
[14] Pedregosa et al. — scikit-learn, JMLR 2011. [15] Elkan — Foundations of Cost-Sensitive Learning, IJCAI 2001.
Full IEEE list: docs/AETHER_SIH26170_References_and_Sources.docx · Repo: github.com/amol16112005/AETHER-SIH26170
Pioneers